## Slide 1: Protean: Resource Efficient Instruction Prefetching
Muhammad Hassan, Chang Hyun Park, David Black-Schaffer
Slides by Muhammad Hassan

## Slide 2: Overview
Problem:
Dedicated intruction prefetchers (DIP) are beneficial for a small subset of applications but claim costly chip area
Key Insight:
When DIP works, Branch Target buffer (BTB) misses can be tolerated
Solution:
Use BTB to store DIP metadata – benefit of DIP without the area cost

## Slide 3: Built-in (free!) Instruction Prefetching: FDIP*
Decode
L1I
ITLB
Exec.
Retire
Fetch
Back-End
BPU/Front-End
FTQ
Head
Branch Predictor
BTB
Demand
Prefetch
*Fetch Directed Instruction Prefetching
BPU run-ahead produce future control-flow
I-cache prefetch targets
Very effective compared to no FDIP
Limited by prediction capability of the BPU
Fetch Target Queue

## Slide 4: Dedicated Instruction Prefetchers (DIPs)
Decode
L1I
ITLB
Exec.
Retire
Fetch
Back-End
BPU/Front-End
FTQ
Head
DIP
Complementary to FDIP
Independent of BPU
Can prefetch far-ahead (than FDIP)
Consumes costly chip area
Increase in dynamic energy
Useless prefetches
Branch Predictor
BTB
Demand
Prefetch

## Slide 5: Are DIPs always beneficial?
Performance
Energy
DIPs only help 5% of applications and hurt 12%
Need to used carefully!
But DIPs claim costly chip area

## Slide 6: Challenges
DIPs benefit a few benchmarks but hurt many
  Insight: We can identify what to do based on perf. counters
  Contribution: Train DT to dynamically switch DIPs on/off
DIPs need in-core costly chip area
  Insight: More BTB space is not needed when DIPs are beneficial
  Contribution: Use BTB to store DIP metadata
  Protean: Using BTB to save DIP metadata – benefit of DIPs without the area cost

## Slide 7: Protean – using BTB for DIP metadata

## Slide 8: Protean: Dynamic FDIP + DIP Front-End
FTQ
Head
DIP
Can we reduce BTB size without hurting performance?
Branch Predictor
BTB
BTB
DIP
BTB | BTB | BTB
12k BTB - Baseline
BTB | BTB | OFF
8k BTB
BTB | OFF | OFF
4k BTB
BTB | DIP | OFF
4k BTB + 4k DIP
BTB | DIP | DIP
4k BTB + 8k DIP
BTB | BTB | DIP
8k BTB + 4k DIP

## Slide 9: Is it okay to reduce BTB size?
Reducing BTB size doesn’t hurt performance
BTB size of 4k is not enough
Insensitive to BTB size
Takeaway 1: For these applications, BTB space can be traded for DIP metdata
Takeaway 2: For some benchmarks, BTB size should not be reduced below 8k!
Best we can do with instruction prefetching
8k BTB performs similar to 12K BTB

## Slide 10: Understanding BTB misses
L1I
ITLB
Decode
Exec.
Retire
Fetch
Pipeline
Prefetch
Head
FTQ
BTB miss
Resteer (Pipeline Flush)
Detrimental to Performance – long front-end stalls
Branch Predictor
BTB
Demand
Prefetch
STOP

## Slide 11: Post Fetch Correction (PFC)*
L1I
ITLB
Decode
Exec.
Retire
Fetch
Pipeline
Prefetch
FTQ
BTB miss
Post-Fetch Correction (PFC)
Certain BTB misses can be corrected at decode stage
Branch Predictor
BTB
Demand
Prefetch
Key takeaway:
PFC makes BTB misses less costly
Only for direct branches
STOP
* “Rebasing Instruction Prefetching: An Industry Perspective” IEEE CAL 2020

## Slide 12: Indirect branches problem with 4k BTB
Impossible to implement
Effect of PFC on indirect branches
Larger BTB misses, latency PFC cannot hide
Key takeaway:
4k BTB suffers more from indirect branch misses which cannot be corrected by PFC

## Slide 13: Benefits of dynamic configuration
No single static configuration achieves the best performance/energy
Dynamic configuration is required!

## Slide 14: Choosing different optimizatons
Max Perf.
Min. Energy
Max. Euclidean Dist. -> Score
Balance
Performance
Energy
How can we optimize for both metrics?

## Slide 15: Different Optimization choices
Insensitive (Nothing to be gained)
Sensitive-good (Potential to be gained)
Balanced optimization
Performance optimization
Energy optimization
Different optimization goal selects different configurations

## Slide 16: Choosing the correct configuration at runtime
Separate Decision Tree for each optimiation (Perf., Balance, Energy)
15 different performance counters
  With 5 performance counters, accuracy suffers
DT’s are evaluated after every 20M instruction interval
> 95% accuracy
4KB DRAM budget
Robust performance even with less training data
Performance optimization top 3 perf. counters:
  L1I MPKI
  ITLB MPKI
  STLB instruction MPKI
Execution
Interval
Performance Counters
Classification Algorithm
Execution
Next Configuration

## Slide 17: Results – Performance Optimization
Oracle
Decision Tree
Sensitive-bad: Mispredictions can hurt, but DT was accurate enough
Sensitive-good benchmarks:
Performance Optimization: 86% of the potential
Balanced Optimization: 96% of the potential
Energy Optimization: 98% of the potential

## Slide 18: Protean: Minimal cost Instruction Prefetching
FTQ
Head
DIP
Branch Predictor
BTB
BTB
DIP
DIPs are only benefical for a few benchmarks but claim costly chip area
We can identify benchmarks that benefit from DIP
When DIP works, BTB misses can be tolerated
Use BTB to store DIP metadata
Investigated 3 different optimization goals
Defined a scoring system to identify the best configuration
Use DT to predict best configuration using perf. counters
Demand
Prefetch
L1I
ITLB
Decode
Exec.
Retire